## Slide 1
CS-423 Computer Graphics

## Slide 2: What computers do....
Process, transform, communicate information
Aspects of Communication
  Origin (where does it come from?)
  Throughput (how long will it take to get here?)
  Latency (how long do I have to wait before something happens)?
  Presentation (what does it look like?)
Computer Graphics is...
the technology for presenting information

## Slide 3: Computer Graphics
Today, Computer Graphics has become the predominant form of computer output.
Even the text on most computer screens are "rendered" using computer graphics methods.

## Slide 4: Computer Graphics
Computer Graphics is all about drawing pictures on computers, also called rendering.
The pictures can be photographs, drawings, movies, or simulations
  -- pictures of things which do not yet exist and maybe could never exist.
  -- Or they may be pictures from places we cannot see directly, such as medical images from inside your body.

## Slide 5: Computer Graphics
Drawing pictures on computers – “rendering”
Final output – colored pixels

## Slide 6: Computer Graphics
The goal of computer graphics is to:
  Create (synthetic) images indistinguishable from reality
  Animations that are scientifically sound

## Slide 7: What will you get out of this course?
Learn to draw on a computer (and appreciate what is involved in this task)
What this course is not…
  It is not an art class
  It is not a game design course

## Slide 8: Pixels
A picture is produced by an n x m array of pixels (picture elements)
Also known as raster

## Slide 9: Color Image (RGB)

## Slide 10: Pixels
Painted on the screen by CRT
  Random scan
  Raster scan

## Slide 11: CRT
Most common display device a few years back
Evacuated glass bottle
Heating element (filament)
Electrons attracted to focusing anode cylinder due to strong positive charge on outer surface
Vertical and Horizontal deflection plates. The first set displaces the beam up and down, and the second displaces the beam left and right.
Beam strikes phosphor coating on front of tube

## Slide 12: CRT
The phosphor then emits a small spot of light at each position contacted by the electron beam.
The light emitted by the phosphor fades very rapidly.
One way to keep the phosphor glowing is to redraw the picture repeatedly by quickly directing the electron beam back over the same points.
This is called refresh CRT.

## Slide 13: CRT
The total number of points that can be plotted horizontally and vertically on a CRT is referred to as resolution.
The ratio of vertical points to horizontal points necessary to produce equal length lines in both directions on the screen is called aspect ratio of video monitor.

## Slide 14: Raster Scan Displays
Based on television technology.
The electron beam is swept across the screen one row at a time from top to bottom.
During this scan, the beam intensity is turned on and off to create a pattern of illuminated spots
Picture definition is stored in a memory area called frame buffer.

## Slide 15: Raster Scan Displays
The frame buffer holds the set of intensity values for all the screen points.
Stored intensity values are then retrieved from the frame buffer and painted on the screen one row at a time
One bit per pixel in black-and-white system (bitmap)
24 bits/pixel for color systems (pixmap)
Refresh rate of raster scan display is about 60 frames per second

## Slide 16: Interlacing
On some raster scan systems, each frame is displayed in two passes using an interlaced refresh procedure.
In the first pass the beam sweeps across every other scan line from top to bottom.
After the vertical retrace the beam sweeps out the remaining scan lines.

## Slide 17: Interlacing
Interlacing allows us to see the entire screen displayed in one-half the time it would have taken to sweep across all the lines at once.
Used with slow refresh rates.
Allows higher resolutions – that is scan more lines with less expensive components
The fading of phosphors between each pass is noticeable, causing the screen to flicker

## Slide 18: Random Scan Display
CRT has the electron beam directed only to the parts of the screen where a picture is to be drawn.
Draw a picture one line at a time and also referred to as vector or calligraphic displays
Refresh rate depends upon the number of lines to be drawn
Picture definition is stored as a set of line drawing commands in refresh buffer.

## Slide 19: Color Video
More complicated.
The phosphors on the face of a color CRT are laid out in a precise geometric pattern.

## Slide 20: Color Video
Within the neck of the CRT there are three electron guns, one each for red, green, and blue (the actual beams are all the same color-- invisible).
There is also a special metal plate just behind the phosphor, called a shadow mask.
This mask is aligned so that it simultaneously allows each electron beam to see only the phosphors of its assigned color and blocks the phosphor of the remaining two colors.

## Slide 21: LCDs
Used in calculators, laptops.
Produce a picture by passing polarized light from the surroundings or from an internal light source through a liquid crystal material that can be aligned to either block or transmit the light.
Liquid crystal is a compound that has a crystalline arrangement, yet it can flow like a liquid.

## Slide 22: Object Rendering
Modeling:
  How to represent objects  mathematical specification of shape and appearance properties
Rendering
  How to create shaded images from 3D computer models
Animation
  How to represent motion  through sequence of images

## Slide 23: Modeling

## Slide 24: Modeling
Deals with the mathematical specification of shape and appearance properties.
For example, a coffee mug might be described as
  a set of ordered 3D points along with some interpolation rule to connect the points
  and a reflection model that describes how light interacts with the mug

## Slide 25: Rendering
creation of shaded images
from 3D computer models
Compute camera view
Clipping
Hidden line removal

## Slide 26: Rendering
Shading
Lighting
Shadows

## Slide 27: Goal of Computer Graphics
Create (synthetic) images indistinguishable from reality
Animations that are scientifically sound

## Slide 28: Goal of Computer Graphics

## Slide 29: Goal of Computer Graphics

## Slide 30: Goal of Computer Graphics

## Slide 31: Goal of Computer Graphics

## Slide 32: Goal of Computer Graphics

## Slide 33: Goal of Computer Graphics

## Slide 34: Goal of Computer Graphics

## Slide 35: Final Fantasy
The first computer-generated animated motion picture with photo-realistic characters

## Slide 36: Image Based Rendering
Generate synthetic images from real images
Structure (3D) has to be extracted for realistic rendering
So far, moving towards more realistic renderings:
Ray tracing
Radiosity
Image-Based Rendering
But that is not the goal of ALL computer graphics

## Slide 37: Another Goal
Creating a new reality
Or simulating non-reality
Aesthetically pleasing
Entertainment or Education value

## Slide 38: Another Goal

## Slide 39: Another Goal

## Slide 40: Application areas
Movies
If you can imagine it, it can be done with computer graphics.

## Slide 41: Movies
Luxo Jr : a desk light playing with a ball.
  The first three-dimensional computer animated film to be nominated for an Academy Award, in addition to winning 20 awards at international film festivals.
  Includes several technical achievements in computer animation, like self-shadowing, where an image accurately casts shadows onto itself.

## Slide 42: Movies
Great visual effects, e.g. bullet time
Concept is to play with motion and time in video or movie. The reason is to slow down or even freeze the time and let the audience see things around it more clearly at that particular moment in time.

## Slide 43: Movies

## Slide 44: Movies

## Slide 45: Games
Games are an important driving force in computer graphics.

## Slide 46: Games
Games are an important driving force in computer graphics.

## Slide 47: Games

## Slide 48: Medical imaging
Computer graphics plays a significant role in saving lives.
The range of application: tools for teaching and diagnosis, all the way to treatment.

## Slide 49: Computer Aided Design
Computer graphics has had a dramatic impact on the design process.
Today, most mechanical and electronic designs are executed entirely on computer.
Increasingly, architectural and product designs are also migrating to the computer.

## Slide 50: Scientific Visualizations
Computer graphics makes vast quantities of data accessible.
Numerical simulations frequently produce millions of data values. Similarly, satellite based sensors amass data at rates beyond our abilities to interpret them by any other means than visually.

## Slide 51: Simulation

## Slide 52: Graphical User Interfaces
Graphical elements such as windows, cursors, menus, and icons are so common place it is difficult to imagine computing without them.

## Slide 53: Program 1 – Reading / Writing Images
In this Program, you will learn…
  Concept of R, G, B colors
  Image manipulation in code
  Reading and writing images in .ppm format

## Slide 54: PBM, PGM, PPM Format
Portable Bit Map Formats
Simple Image header in ASCII
Image data in either ASCII or Binary
.PGM for Grayscale images
.PPM for Color (RGB) images

## Slide 55: You will have to…
Write code to Read/Write BINARY .ppm and .pgm files
Images will be available through msteams

## Slide 56: PPM Format
Header
  P6
  # Created by IrfanView
  320 240
  255
  –ˆc™‡d˜ˆf™‰h_‡f_‹h›S+XR1ZQ3YSY
  r g b r g b r g b r g b r g b r g b r g b r g b

## Slide 57: PPM, PGM Format
Magic Numbers for format identification
  P2 - ASCII PGM
  P3 – ASCII PPM
  P5 – Binary PGM
  P6 – Binary PPM

## Slide 58: Tasks
Read in the given .ppm and .pgm image files and load the data in any data structure of your choice, i.e. 1d arrays, 2d arrays, or array of structures etc.
From that data structures create a new copy of image with a different filename
HOW TO VIEW
  Any .ppm viewer
  IrfanView – (from irfanview.com)

## Slide 59: Tasks
Subtract ambient. Make sure the intensity value doesn’t go beyond 0. This way you will be able to subtract two images other than ambient.
Extract single/two color layer(s)
Negative
Greyscale
Combine two images
Make a movie.

## Slide 60: Deliverables
DUE: Sunday, March 2, 2024 at 11:00pm.
Code, executable… should take image names at run-time
Submit a report too.